Drive Laser Meetings

Date: 11-18-04

Attendees: Eric Bong, Richard Boyce, David Dowell, Leif Eriksson, Sasha Gilevich, Alan Miahnahri,

Carl Rago, John Schmerge

Tasks									Person Responsible

1.   Laser room should have opening at ceiling			Carl

2.   Everybody agreed on, Alum. Tubes and

O-ring-rubber (Viton) for sealing flanges.			Alan, Leif

- Components width should be larger than

Top plate diameter	.					Alan, Carl

.

4.  Stress analysis on lifting bolt.					Alan, Leif

5.  David and Stan will go over the shielding requirements.

6.  Add drain tube inside Transport tube assembly.			Alan, Leif

6.  Check to see if the transport hole is clear

If required remove rust and apply anti rust coating.  		 Carl

7.  Shutters (two locations). Inside a box, tamper proof.		 Alan, Sasha, David

8.   Safety requirement is 3 feet space around optics table.

Alan will check if it is possible.					Alan, Richard, Sasha

9.   Check Beam path interference with Cathode Gun.		 Richard, Alan, Sasha, John, David

22.5˚  V.S. 18˚.

10.  2” optics window							Alan, Sasha

11.   Diagnostic components.	No work done  			Alan, Sasha, David

- Design safety

  - Earth quake						Leif

  - Laser safety						Sasha

  - Radiation						Dave

  - Design Implement					Alan

13.  Design a cover for transport tubes during construction.		Alan, Carl