Noteworthy Practices (NP):

- Handling of PEP Utility relocation water leak: Water line leak was found to be old transite line (domestic/potable water & not the new CT water line). NP is the process in which the situation was handled. Turner in conjunction with LCLS prepared a detailed methodical plan.

- Fall protection noted in NEH for worker installing decking bracing.

Access tunnel portal (East) behind bldg. 750 – note ventilation line now installed.

Road-header on site at UH (West) Portal

Brass-tag board (East Access Tunnel Portal at entry) being used to track number of personnel underground (NP).

Utility water leak (PEP) – line on far right is the domestic water line which has the leak. (two larger lines to the left are the newly installed CT water lines).

Fall protection being worn by worker installing temp. steel decking support in the NEH (NP)

Forms and rebar for BTH – jobsite condition very good (NP)

# Text boxes

Name: J. Logan - D.O.E.

Date: 4/4/07

LCLS Construction Safety Inspection Comments/Observations:

Site Work in-progress:

Work in-progress:

Research Yard: Formwork being hung, and rebar installed in preparation for BTH slab pour – west end.

NEH: Temp. support for steel decking being installed, 40 yd3 pour around elevator shaft in-progress (pumper on site)- new crane on-site for lifting NEH metal decking

PEP: Water line repair in-progress – see Noteworthy practices

Access Tunnel Portal (East): Mining/mucking in-progress, tunnel headwall @ 50 ft., ventilation system now installed, brass-tag board in use for entry. Sweeper being used to mitigate/suppress dust.

Time: 8:00 AM

Date: 3/22/07

DOE/SSO LCLS Construction Safety Inspection Log

Identified Hazards:

Hazard identified on JSA

Hazard Controls in-place: Yes X    No ___

JSA Complete

Completed    Yes X      No ____

Completed for

Contractor  -- Permits approved

Yes X    No      N/A  excavation approved

Safety Process Observations: (noted during walkthrough)

##### East Portal: noted Gradall teleboom handler with scissor lift, not positively secured (tied-off) nor resting against mast – Turner corrected during walkthrough.

Site Notes and Photographs

Safety Process Observations Follow-up (Previous Inspection)

##### NEH: Nicked electrical cord on job-box – done last week, removed during walkthrough

##### East Portal: Turner at SLAC’s request to investigate provisions for dust control at tunnel entrance where mucker and front loader are in operation for tunnel spoils off-hauling.- done, sweeper being used to remove dust.