Noteworthy Practices (NP):

- Jobsite Housekeeping: housekeeping at all jobsites is excellent – see photo below of the RSY jobsite.

Concrete slab pour at BTH in the Research Yard (RSY)

Extinguisher/eyewash station (RSY – belongs to Turner).

BTH Construction – view looking East toward UH Portal

Note: Sacks in the foreground are sandblasting materials. Verified that Kleen-Blast (no free silica) material is being used. Sandblaster wearing facemask – recommend APR level respirator be utilitzed – LCLS should check mfg. recommendation.

Access tunnel portal (Mucker shown on left).

Mucker carrying mobile mixer for shotcrete (Access Tunnel Apron)

# Text boxes

Name: J. Logan ,T. Rizzi

Date: 4/24/07

LCLS Construction Safety Inspection Comments/Observations:

Site Work in-progress:

Work in-progress:

Research Yard: Slab pour in-progress (BTH), concrete pumper on-site. Sandblasting starting.

NEH: Rebar install at NEH – 2nd floor (Rod busters working)

PEP: I-beam braces installed for temporary bracing of utilities. Grading in-progress above Turner City (2 scrapers, dozer, and compactor in operation).

Access Tunnel Portal (East): tunnel work in-progress, mucker was removing shotcrete mixer (50 ft. length limit on slick lines).

Time: 8:30 AM

Date: 3/22/07

DOE/SSO LCLS Construction Safety Inspection Log

Identified Hazards:

Hazard identified on JSA

Hazard Controls in-place: Yes X    No ___

JSA Complete

Completed    Yes X      No ____

Completed for

Contractor  -- Permits approved

Yes X    No      N/A  excavation approved

Safety Process Observations: (noted during walkthrough)

- RSY: Eyewash bottle missing (Turner eyewash station)- Turner agreed to provide bottle.

- Access Tunnel (East portal): fire extinguisher inspection tag out of date (dated 2006) – Turner agreed to inspect.

- Request LCLS Safety to verify if dust mask is sufficient for use with sandblasting (use of Kleen-Blast) per mfg. recommendations.- MSDS calls out for NIOSH approved mask, garments, and head-gear to be used during blast operations.

Site Notes and Photographs

Eyewash bottle missing - RSY

Safety Process Observations Follow-up (Previous Inspection)- all addressed

##### Done - Wire rope “Bird-caged” removed from jobsite (CCR T8, 5042(a)(1))

##### Done - 90-degree rebar capped with rebar end caps

##### Done - Discussed non-slip application to ladder, concern expressed by Conco (concrete sub) that it could peel off – admin. controls (3-point contact) will be used.

Extinguisher needs re-inspection