Noteworthy Practices = (NP):

- Worker mixing grout for soil nails was wearing fit-checked dust mask (N95-type) – Condon-Johnson (NP).

Worker in unsupported hole – depth @ 4ft (less than 5 ft.)@ 3.1 building – extracting old concrete block.

Hole cover marked, but not secured to prevent inadvertent movement (hole depth approx. 32 feet) @ 3.1 Bldg. site.

Holes are drilled for utility shaft install for tunnel.

Recommended to cap exposed soil nails to mitigate potential impalement injury, etc. – TC notified Condon-Johnson (FEH open cut soil nail wall site)

Conco use of foam caps for large rebar at BTH (NP)

UH Tunnel Portal (2 shift work now in-progress on UH Tunnel)

Corrective action follow-up: caps on FEH soil nails (follow-up on 5/17-07 action).

# Text boxes

Name: J. Logan

Date: 5/17/07

LCLS Construction Safety Inspection Comments/Observations:

Site Work in-progress:

Work in-progress:

Research Yard: Form build in-progress for wall pour (Conco). Tunnel mining continuing at UH Tunnel.

NEH: Forms being hung for upper wall pour (Conco)

PEP: Shafts being installed at Bldg. 3.1 site (adjacent to FEH – Malcolm Drilling). Grouting for soil nails in-progress at FEH (Condon-Johnson).

Time: 1:00 PM

Date: 3/22/07

DOE/SSO LCLS Construction Safety Inspection Log

Identified Hazards:

Hazard identified on JSA

Hazard Controls in-place: Yes X    No ___

JSA Complete

Completed    Yes X      No ____

Completed for

Contractor  -- Permits approved

Yes X    No      N/A  excavation approved

Safety Process Observations:

- Hole covers not secured to prevent inadvertent movement at Bldg. 3.1 site – TC agreed to secure (hole depth approx. 30 feet, 4 ft. dia.).

- Recommended to cap soil nails to mitigate potential for impalement/abrasion injury (OSHA subpart Q). Caps have been installed, per 5/21/07 e-mail – see photo at the end of this report.

Site Notes and Photographs

Safety Process Observations Follow-up (Previous Inspection)- all addressed

- Safety question NEH: does the fall protection anchor point on the NEH wall forms meet the Cal-OSHA 5,000 lb requirement? SLAC stated OK.