Noteworthy Practices (NP):

- Dust at portal (East Access Tunnel) is being cleared – improved.  Turner also asked that dust at west Portal being misted for suppression. Subcontractor (Turner) is aware of the dust issue, and is implementing process controls for dust suppression.

Comments:

- Hoisting & rigging process controls (slings): Need to ensure that wire-rope and other slings are inspected daily before use (Ref. CCR T8, 5043) – this should also include inspection of end fitting(s) and other components in the sling-assembly.

- Scrapers: scrapers seemed to be operating at high speed on fill site haul road – ensure traffic control pattern in place, and haul unit cycle times do not create unsafe equipment speeds.

NEH 2nd floor: 90-degree rebar with unprotected edges – recommended end caps or equal (14 gauge steel or wood trough) be installed (CCR T8, D. 1712).

PEP Utility excavation site: Wire rope sling with unwoven strands – “Bird-caged” – recommended removal from jobsite.

Job-built ladder at NEH – recommended non-slip surfacing be applied to cleats. (ladder for 2nd story access).

Road-header in operation at West (RSY-UH) Portal

BTH rebar mat prior to floor-slab pour (view looking West toward LINAC).

Teleboom handler being used at RSY for BTH slab construction – driver was wearing seat-belt (NP)

# Text boxes

Name: J. Logan - D.O.E.

Date: 4/17/07

LCLS Construction Safety Inspection Comments/Observations:

Site Work in-progress:

Work in-progress:

Research Yard: Rebar install in preparation for slab pour, road-header in operation at West (RSY) Portal.

NEH: Rough-in utility work (Cupertino Electric)

PEP: Installation of I-beam braces at excavation site. Scrapers & dozer in operation at fill site above Turner City.

Access Tunnel Portal (East): Mining excavation using road-header in-progress, heading at approx. 135 ft. (depth), brass-board in use, ventilation system in operation.

Time: 2:00 PM

Date: 3/22/07

DOE/SSO LCLS Construction Safety Inspection Log

Identified Hazards:

Hazard identified on JSA

Hazard Controls in-place: Yes X    No ___

JSA Complete

Completed    Yes X      No ____

Completed for

Contractor  -- Permits approved

Yes X    No      N/A  excavation approved

Safety Process Observations: (noted during walkthrough)

- NEH: Recommended rebar end caps or other (trough) means to protect ends on 90-degree rebar to mitigate impalement/abrasion hazard.

- PEP Ring road – found wire rope sling being used to lift 9,500 lb steel beams had wire strands unwound in one section (“Bird-caged”) – recommended tag & removal from jobsite (Ref CCR T8, 5042(a)(1)).

- NEH: Job built ladder for 2nd story access, recommended non-slip surface be applied to 2x4 rungs to remediate slip hazard (especially during wet-conditions). Ladder was tied off at the top, and blocked at the bottom, ladder under 30 ft. length (1676(d)).

Site Notes and Photographs

Safety Process Observations Follow-up (Previous Inspection)

##### East Portal: noted Gradall teleboom handler with scissor lift, not positively secured (tied-off) nor resting against mast – Turner corrected during walkthrough (4/4/07).

Ladder blocked at bottom (NP)