Noteworthy Practices (NP):

- Turner has placed a safety board, and safety suggestion box outside their trailer (NP)

- Good traffic control observed during major concrete pour (NP)

- Inspected utility trench installation work adjacent to NEH (Cupertino Electric), competent person on site, and trench benched, with ladders available for egress. Area was also well flagged, and do not enter warning signs posted. JSA was dated and signed (5/3/07)(NP)

- Noted Affholder gas monitoring record current, and posted at the portal entrance (inspected UH portal) (NP)

Turner Safety Suggestion Box (located outside Turner Trailer main entrance) (NP)

NEH Elevated Deck Concrete Pour (approx. 1,000 cubic yard concrete pour)

CUP Electrical utility installation: excavation jobsite perimeter flagged, signed, and excavation benched. Ladder shown for egress, & competent person site. JSA was signed.

View standing on the BTH slab, looking East, at the UH Tunnel Portal.

Noted in afternoon visit, the ramp had mid-span support added (corrective action finding implemented).

# Text boxes

Name: J. Logan

Date: 5/3/07

LCLS Construction Safety Inspection Comments/Observations:

Site Work in-progress:

Work in-progress:

Research Yard: Prep for next BTH pour, mucker removing spoils from UH tunnel, and shotcrete being mixed.

NEH: NEH elevated deck pour (1,000 cu yds) in progress

PEP: No activity, cutback complete for 3.1 building

Access Tunnel Portal (East): Not inspected, per OAC Meeting, the Access Tunnel is at 200 ft depth, and the UH Tunnel is at 50 ft depth. Air monitoring records were reviewed (O2 @ 20.9%, CFM = 32,500 – calc for personnel and diesel equipment operating underground. Tunnel to go on 2nd shift at the UH by 5/14/07.

Time: 10:30 AM

Date: 3/22/07

DOE/SSO LCLS Construction Safety Inspection Log

Identified Hazards:

Hazard identified on JSA

Hazard Controls in-place: Yes X    No ___

JSA Complete

Completed    Yes X      No ____

Completed for

Contractor  -- Permits approved

Yes X    No      N/A  excavation approved

Safety Process Observations: (noted during walkthrough)

- BTH: Fall protection harness placed on the ground – potential for damage (Ensure inspect before each use, ref. CCR T8, 1670(b)(15)).

- BTH: Elevated (2 ft) cross over deflecting too much – suggested Conco reinforce mid-span to prevent deflection – possible slip/trip hazard – Noted done in afternoon walkthrough.

Site Notes and Photographs

Orange Affholder (Tunnel mining subcontractor) Air monitoring form, showing current record of gas testing, and CFM calculations (Oxygen was at 20.9%, OSHA range is 19.5% to 23.5%).Form is posted at tunnel portal entrance on clip board (NP)

Safety Process Observations Follow-up (Previous Inspection)- all addressed

- RSY: Eyewash bottle missing (Turner eyewash station)- Turner agreed to provide bottle.

- Access Tunnel (East portal): fire extinguisher inspection tag out of date (dated 2006) – Turner agreed to inspect - Done.

- LCLS verify dust mask OK for sandblasting – Done, Nozzle man is wearing a SAR Blasting Hood when operating the system. The helper wears the N-95 Particulate Respirator.