Noteworthy Practices (NP):

Building 3.1 (Utility) – note stakes are for shaft placement (tunnel shafts). Plan is to hydro-seed banks.

Darker color clay deposit shown above.

Bldg. 3.1 per Turner has an 8” slab on grade – metal frame building.

Open cut in-progress at the FEH jobsite

Rod-busters at work in BTH jobsite (Area 7)

Dirt-berm at FEH site – recommend adding a K-rail on heavy traffic side – add rail at yellow line for example.

K-rail (concrete) typical view only

# Text boxes

Name: J. Logan

Date: 5/10/07

LCLS Construction Safety Inspection Comments/Observations:

Site Work in-progress:

Work in-progress:

Research Yard: Deck pour in-progress (Area 2B complete (500 yd3), start Area 1 pour tomorrow)

NEH: Prep. for forms for next pour in progress

PEP: Open cut excavation in-progress (excavator + articulated haulers) at FEH.  Bldg. 3.1 shafts have stakes placed.

Time: 1:00 PM

Date: 3/22/07

DOE/SSO LCLS Construction Safety Inspection Log

Identified Hazards:

Hazard identified on JSA

Hazard Controls in-place: Yes X    No ___

JSA Complete

Completed    Yes X      No ____

Completed for

Contractor  -- Permits approved

Yes X    No      N/A  excavation approved

Safety Process Observations: (no findings – have some recommendations):

- Place a K-rail in addition to dirt berm at FEH open cut site, in event car/truck looses braking capability.

- Use a spotter when starting/ending a work shift for workers at NEH who have to walk on haul road. Articulated haulers have limited rear vision.

- Use dust masks if there is wind when sweeping up fines from sand-blasting

- Place end caps on rebar - monitor

Site Notes and Photographs

Safety Process Observations Follow-up (Previous Inspection)- all addressed

- Ramp stabilized during walkthrough for BTH access

Clay deposit area