Spatial Profile Flattening of Picosecond UV Laser Pulses Using Aspheric Refractive Optics

Paul R. Bolton, Brendan F. Murphy,

and John F. Schmerge,

Stanford Linear Accelerator Center, Stanford University, California

(SPIE Beam Shaping Conference August 3-8, 2003)

I.	Introduction - Motivation

II.	Aspheric Refractive Technique

III.	Experimental Setup for Single Shot UV Case

IV.	Observations and Analysis

V.	Implementation Issues for RF Photoinjectors

VI.	Summary

I.	Introduction - Motivation

RF Photoinjectors can produce high quality

electron beams at high charge levels

injector of choice for SLAC’s Linac

Coherent Light Source (LCLS) which is a

proposed xray FEL facility

electron beam properties depend critically on

properties of laser pulses irradiating the

photocathode

drive laser for RF photoinjectors is then

a critical, highly leveraged component of LCLS

specifically: RF photoinjector designs call for laser

irradiation with nominally

uniform spatial and temporal profiles –

where spatial uniformity requirement

is > 90% for LCLS

II.	Aspheric Refractive Technique

IBM developed an aspheric refractive technique using a pair of positive lenses which redistributes laser energy to larger radii with a collimated output beam * :

to

=  input Gaussian profile          (with azimuthal symmetry)

= output ‘flattenned’ profile    (with azimuthal symmetry)

(Ref. 1  J.A. Hoffnagle and C.M. Jefferson,  Applied Optics 39[30], 5488 (10/20/00))

and

(input profile model is Gaussian and output is Fermi-Dirac)

R = HWHM,

is a dimensionless shape parameter = R/W  (shape parameter,W)

is spotsize

Lens pair deign is determined by     (i)    collimation requirement

(ii)   Snell’s Law

(iii)  ray tracing function (radial energy redistribution)

* flattener unit now marketed by NRC

relationship between efficiency (fraction of energy contained within a fixed radius) and spatial profile uniformity is profile dependent

‘flattened’ case  -  significantly more efficient for given

uniformity requirement

-  fluence on optics is reduced and

scales as:

Hoffnagle and Jefferson had examined the flattening doublet using cw waveforms at 532  and 257 nm 1

Issues Relevant to Single UV Pulses:

Shot-to-shot variations (profile, size, energy, steering)

Higher intensities

Spectral bandwidth – dispersive effects still be small

Pulsed results complement cw data especially because 	the same flattener was used in both cases where 1,2 :

Input Spotsize,  = 2.4 mm  and  R = 3.3 mm

(Ref 2  B.F. Murphy et al., SLAC LCLS-TN-03-4)

III.	Experimental Setup for Single Shot UV Case

CPA laser system at SLAC’s Gun Test

Facility (GTF) – uv generated by fourth

harmonic conversion of compressed 1054 nm

light at a 2.5 Hz repetition rate

need to enable single shot comparison of incident

(Gaussian) and ‘flattened’ beam spatial profiles

UV pulses features:		80 microJoule level

2  psec  duration

incident spotsize of 2.4 mm

rep. rate = 2.5 Hz

bandwidth, 0.5 nm

IV. Observations and Analysis

Both the cw green and pulsed uv measurements 	demonstrated clear profile flattening

Alignment of the IBM flattener was critical

Observed important shot-to-shot variations in pulsed 	case that are largely attributed to lateral shifting of the 	incident pulse off  axis (this shift is in turn attributed 	to uv beam steering over a length of about 2 meters)

Cw green (IBM)			Pulsed uv (SLAC)

R /		1.4						1.2

Input 	 	  3						  4

Output  		18						16

Plateau			0.95						0.99

Min/max ratio

(of linear fit & excluding noise)

VI. Summary

fixed profile shaping with aspheric refractive optics 	is feasible for photoinjector drive lasers :

- implement as a three element section

(spatial filter +flattener +trimmer)

- steering jitter at input must be controlled

- spatial filtering of input is essential

- input spotsize set to fixed design value

- this is the nonadaptive case

drive laser use can be with comparable bandwidths,	higher intensities, and higher repetition rates:

- can be used for ir or uv wavelengths

- may require evacuation between lenses

(positive lens pair)

- anticipate net efficiencies near 70 %

(85 % for spatial filtering

and 85 % for downstream trimming)

- relayed transport over extended lengths

is critical due to strong diffractive effects

02/12/04 Update from NRC rep *:

- currently available at $ 4950.

is unit designed for = 4.7 mm and

output FWHM = 8.1 mm (needs to be verified)

and AR coated for ‘ir’

- available in May-June ’04 timeframe

is same unit as above but AR coated for ‘uv’

- units designed for other input spotsizes (custom) 			  available sometime in 2005 (i.e. “well into…”)

- no final decision on possible price break option

for us in exchange for test data

A good plan is to use one of these with uv conversion prototyping

(eg. ANL effort)

Gratefully acknowledge loan of the ‘flattener’ unit and valuable assistance from John Hoffnagle and Michael Jefferson of IBM