First Step: Clarify LCLS specs on uv pulse & drive laser specs for SOW

UV specs to check/finalize:

wavelength 		- 260 to 270 nm (bias toward lower end - Schmerge)

energy tolerance	- 2 %

spot radius		- 1.2 mm

power profile		- plateau flatness 5% rms (Emma, Zhirong, Juhao)

power profile		- rise/fall time 0.5 to 1.0 psec (Emma, Cecile)

timing jitter		- < 0.5 psec shot-to-shot

power profile		- FWHM 10 psec to 18 (or 20) psec

IR specs to check/finalize:

energy			- 25 mJ (check transport, quantum and grating efficiencies)

energy tolerance	- 1% (scaled from uv, need correct slope data *)

spatial profile		- < 10% (scaled from uv, need correct slope data*)

power profile		- plateau nominally uniform with <5% rms flatness but 					  adaptable  (scale from uv , need correct slope data *)

power profile		- rise/fall time 0.5 psec to 1 psec (scale from uv , need correct 				  slope data*)

timing jitter		- < 0.5 psec shot-to-shot or better ?