First Step: Clarify LCLS specs on uv pulse & drive laser specs for SOW

UV specs to check/finalize:

wavelength 		- 260 nm (and bandwidth is determined by details of 					 ‘ir’ shaping requirements and THG  process)

where :

- a nonzero chirp is preferably positive for preserving flat current profile

(less sensitive to uv flatness and for

- .33 nm/psec  with 20 or 30 degree 	launch the uv slope changes from positive to 	negative)

- if we push to 255 nm then:

QE up by ~ 15% (Schmerge 4/01 talk)

TE up by  ~ 10%  for flat case  										       (Schmerge 4/01 talk)

Cryo cooled TiS amplifiers prefer to 							     run near 760-765 nm  (H.Kapteyn)

YES – go to 255 nm for uv spec

energy tolerance	- 2 %

spot radius		- 1.2 mm

power profile		- plateau flatness 5% rms (Emma, Zhirong, Juhao)

(J. Wu et. al. writing report on this)

power profile		- rise/fall time 0.5 to 1.0 psec (Emma, Cecile)

timing jitter		- < 0.5 psec shot-to-shot

power profile		- FWHM 10 psec ( nom. 10 psec , adjustable to 20 psec)

Repetition rate		-  >120 Hz  (for preamplifier in particular and gun test 				lab in mind) ? NO use 120 Hz for final amp!

IR specs to check/finalize:

energy			- 25 mJ (check transport, quantum and grating efficiencies)

energy tolerance	- 1% (scaled from uv, need correct slope data *)

spatial profile		- < 10% (scaled from uv, need correct slope data*)

power profile		- plateau nominal uniform flatness (but adaptable)

<3% rms (possibly 5% )

(scale from uv , need correct slope data *)

power profile		- rise/fall time 1.5 psec

(scale from uv , need correct  slope data*)

timing jitter		- < 0.5 psec shot-to-shot or better ?