# Wakefield Computations for LCLS PhotoInjector

in preparation for CD2b Review

(Summary based on C. Limborg’s 11/21/03 Memo, Deadlines reviewed by D. Dowell)

LCLS Tasks (C. Limborg, S. Gierman):

L.1 - GTL 1st Instrumentation Tank (Deadline: 2/1; Cecile – ABCI, MAFIA)

YAG1 screen, Electro-optics (EO) device, a pump and possibly a pepper pot mask.

Determine

- If RF contact is needed for the EO tank mitigation pipe (or the minimum gap required to avoid unacceptable wakefields),

- If the EO measurements be affected by wakefields induced in the cavity containing the two mirrors,

- If wakefield mitigation is needed for a simple YAG1 cross system.

L.2 - Undulator Chamber (Deadline: 3/1; Cecile – MAFIA):

Determine a realistic aspect ratio for the vacuum chamber and if special smooth transitions are needed.

L.3 - Other Single Elements (Deadline: 3/1; possibly Cecile – MAFIA):

- Wire Scanner (in dispersion free region), (2) OTR crosses,  (3) Valves

ACD Tasks  (C. Ng, Z. Li, Others):

A.1 – S Band Cavity Input Coupler (Deadline: (1) 2/1, (2) 3/1; Zenghai – Omega3P):

(1) Quantify the head-tail kick effect due to transverse fields introduced by the single- feed input coupler (Oblong shape cavity corrects only the amplitude but not the phase),

(2) If transverse kick generates too large of an emittance growth, consider a dual feed design based on the existing SLAC coupler (design modifications to involve L. Bentson)

A.2 - GTL first instrumentation tank (Deadline: 3//1; Cho, Zenghai – Tau3P):

Determine

- If for the pump port, the holes/slots at the bottom of the EO tank generate deleterious wakefields,

- If a Y shape spectrometer chamber generates unacceptable wakefields.

A.3 - DogLeg (DL) Area (Deadline: 3/15; Cho, Zenghai – Tau3P)

Compute transverse wakefields for

- Y shape chamber at DL entrance,

- Y shape chamber at DL exit,

- WireScanner inside DL (also for longitudinal wakes)

A.4 - RF Gun – 1st  Iris Wakefields (Deadline: 4/1):

Using PIC code (probably MAFIA)

Also for  a- accurate evalutation of dimensions

b- effects of higher orders generated from ports

c- dual feed tolerances

………………………………………………………………………………………………

ACTION ITEMS:

- Obtain drawings/CAD files for all elements so meshes can be generated,

- Keep Cecile running on MAFIA,